## Slide 1: Lecture 5 Collecting Data Using Electronic Data Loggers and Environmental Sensors
Jeffery S. Horsburgh
Hydroinformatics
Fall 2016
This work was funded by National Science Foundation Grants EPS 1135482 and EPS 1208732

## Slide 2: Announcements
Assignment 1 due on Thursday
Bring your Arduino kits on Thursday – look for a Canvas announcement about software installation, etc.

## Slide 3: Objectives
Learn basic data collection concepts for hydrologic data
Examine more closely observation dimensionality, including the scale triplet of support, spacing, and extent
Learn the basic datalogger program structure for logging data

## Slide 4: Why do we measure the hydrologic environment?
Detect illegal discharges
Determine compliance with
water quality standards
Reduce health risks for
water consumers
Optimize efficiency of water
treatment
Assessing impact of change
Better understand and predict
natural processes
Detect and quantify
Environmental change
Early warning for natural disasters

## Slide 5
Water Quality Issues
Nutrients (Primarily P)
Sediment
Little Bear River, Utah

## Slide 6: Little Bear River
Pollution Sources: Agriculture Wastewater Treatment
Notes: P sources include fertilized fields, animal waste, WWTP and p-rich soils

## Slide 7: Some Interesting Questions
How do water quality conditions vary throughout a watershed?
What processes (human and natural) drive the variability?
How and why does WQ change over time (minutes - years)
Are WQ conditions getting better or worse?
What might happen in the future?

## Slide 8: What We Really Want
Continuous records of hydrologic variables enable us to observe:
  Timing and magnitude of hydrologic events and constituent fluxes
  What happens from one point in a watershed to the next
  Conditions that drive hydrology (e.g., precipitation, soil moisture, groundwater levels, snow depth and water equivalent…)

## Slide 9: Water Sensors
YSI exo multiparameter sonde
  Temperature
  Dissolved Oxygen
  pH
  Specific conductance
  fDOM
  Bluegreen algae
  …
Forest Technology Systems DTS-12 Digital Turbidity Sensor
  Turbidity
  Temperature
Campbell Scientific CS-450 Pressure Transducer
  Water level
  Temperature

## Slide 10: Dataloggers
Campbell Scientific
  CR206
  CR800
A variety of measurement types
  Analog
  Digital
CRBasic programming language
Table based

## Slide 11: Telemetry
900 MHz Spread Spectrum Radios
Cellular phone modems
Satellite systems

## Slide 12: A Typical Site
Radio antenna
Solar panel
Instrument enclosure
Sensor housings

## Slide 13: Sensor Housings
Permanently mounted to bridge structures
Protect sensors from debris/vandalism

## Slide 14: Instrument Enclosure
Datalogger
Radio
Power supply and charge regulator

## Slide 15: This is all great, but…
How do I go from here…
…to here…

## Slide 16: Scale Issues in Collection and Interpretation of Measurements
The Scale Triplet of Measurements
Adapted from: Blöschl (1996)

## Slide 17: Issues in Data Collection and Interpretation
Adapted from: Blöschl (1996)
Spacing too large – aliasing
*Scan interval too long

## Slide 18: Issues in Data Collection and Interpretation
Adapted from: Blöschl (1996)
Extent too small – trend
*Deploy sensors longer…

## Slide 19: Issues in Data Collection and Interpretation
Adapted from: Blöschl (1996)
Support too large – smoothing
*Data recording/aggregation interval too long

## Slide 20: Which Sampling Frequency is Correct?
The answer is – it depends on what question you are trying to answer
Consider these two questions:
  What is the diurnal pattern of dissolved oxygen concentration in the Logan River?
  What is the effect of cloud cover on photosynthesis and dissolved oxygen concentrations in the Logan River?

## Slide 21: What is the diurnal pattern of dissolved oxygen concentration in the Logan River?
What would you measure?
How often?

## Slide 22: Logan River Dissolved Oxygen Example Raw data – 1 observation per second

## Slide 23: Logan River Dissolved Oxygen Example 1 observation per minute

## Slide 24: Logan River Dissolved Oxygen Example 1 observation every 5 minutes

## Slide 25: Logan River Dissolved Oxygen Example 1 observation every 10 minutes

## Slide 26: Logan River Dissolved Oxygen Example 1 observation every 30 minutes

## Slide 27: Logan River Dissolved Oxygen Example 1 observation every hour

## Slide 28: Little Bear River Dissolved Oxygen Example Hourly Observations

## Slide 29: What is the diurnal pattern of dissolved oxygen concentration in the Logan River?
1-Hz data (1 observation per second) capture the signal, but show sensor noise
1 min, 5 min, 10 min data are all pretty similar
30 min and even hourly data (in all incarnations) are likely adequate

## Slide 30: What is the effect of cloud cover on photosynthesis and dissolved oxygen concentrations in the Logan River?
What would you measure?
How often?

## Slide 31: Logan River Dissolved Oxygen Example Raw Data – 1 observation per second

## Slide 32: Logan River Dissolved Oxygen Example Raw Data + Hourly Instantaneous Data

## Slide 33: Logan River Dissolved Oxygen Example Raw Data + Hourly Data + Hourly Burst

## Slide 34: Logan River Dissolved Oxygen Example Raw Data + Hourly Data + Hourly Burst + Hourly Average

## Slide 35: Logan River Dissolved Oxygen Example Raw Data + 5 minute average data

## Slide 36: What is the effect of cloud cover on photosynthesis and dissolved oxygen concentrations in the Logan River?
The raw data capture the signal, but still exhibit noise from the sensor
Hourly data are not frequent enough to resolve the time scale of the changes
5 min averages look promising for capturing signal and smoothing sensor noise

## Slide 37: The Tradeoffs
High frequency observations
  High temporal resolution of measured variable
  Large volumes of data created
  High power requirements
  High communication bandwidth required
  May be limited by instrument response time
Lower frequency observations
  Efficiency in storage and power
  Lost temporal resolution
  Cannot subsample
  May not be representative (due to aliasing or smoothing)

## Slide 38: Sampling Frequency
Half hourly data subsampled
  -Hourly
  -Daily
  -Weekly
  -Monthly
Half hourly
Hourly
Daily
Weekly
Monthly
Notes: Plots show effect of sampling frequency:
Hourly- still relatively frequent, little information lost.
Daily- general trend and some peaks captured, but fine resolution data lost.
Weekly and Monthly- completely misses the peaks in concentration, periods of greatest contribution to load.
Randomized sampling conducted 10,000 times in order to achieve a distribution of load estimates.
Daily by hour and weekly by day sampling conducted to examine the timing of sampling collection.

## Slide 39: Environmental Sensors
Purpose is to detect events or changes in the environment and provide a corresponding output – usually electrical or optical
Signal is interpreted by or transmitted to a datalogger
  Analog
    A continuous voltage output proportional to the value of the observed variable
    Datalogger must interpret the result
  Digital
    Sensor does all signal processing
    Reports a result encoded as a digital signal to the datalogger

## Slide 40: Dataloggers
Electronic device that records data over time from instruments and sensors
  Generally programmable
  May use integrated or external sensors
  Huge variety available commercially

## Slide 41: Datalogger Programming
Instructions for how and when to:
  Make measurements
  Perform calculations
  Process data
  Communicate data and/or instructions (in more advanced applications)
Encoding instructions to collect observations with the correct support, spacing, and extent to answer your scientific questions…

## Slide 42
Challenges and Adventures in Continuous Monitoring

## Slide 43
It used to be right here!
Have you seen my turbidity sensor?

## Slide 44
Before
After

## Slide 46: Human Challenges
Farmer drives backhoe into river on neighbor’s property and builds dam for his diversion structure.
Lawyers get involved. Farmer pays for new diversion structure and removes dam.

## Slide 47: Variability on the Scale of Hours

## Slide 48: Variability Across Water Years
2007 vs. 2006
  ~ 45% water volume
  ~ 20% TSS mass
  ~ 25% TP mass
Paradise site, water years 2006 and 2007

## Slide 49: TP and TSS Flux 2006
TSS and TP from turbidity using surrogate relationships
~50-60% of the annual load occurs during one month of the year
Little Bear River Near Paradise, UT

## Slide 50: How do Natural Features and Human Activities Affect WQ Conditions?
Spatial distribution of total suspended solids fluxes in the Little Bear River for 2008. The areas of the node markers are proportional to the total suspended solids fluxes, which are expressed in metric tons.

## Slide 51: Summary
It is difficult to understand or manage what we do not measure
Understanding for management requires:
  Collecting data at a spatial and temporal frequency that is consistent with the processes we want to understand
  AND we need data over times scales that will enable us to look at the longer term drivers
    climate change
    land use change
    population growth
  New technologies and monitoring techniques make this possible

## Slide 52: Summary
High resolution (space/time) sensor data enables identification of trends and analysis of hydrologic and water quality behavior that could not be observed by more traditional water quality monitoring
  …but often leaves us scratching our heads!
Large data volumes require cyberinfrastructure and expertise for managing and sharing the data

## Slide 53: Questions?
Support:
EAR 0622374
CBET 0610075