## Slide 1: Data Models
Jeffery S. Horsburgh
Hydroinformatics
Fall 2016
This work was funded by National Science Foundation Grants EPS 1135482 and EPS 1208732

## Slide 2: Announcements
Assignment 2 – Due Thursday
Install MySQL and MySQL workbench BEFORE class on Thursday (instructions on Lecture Materials Canvas page)

## Slide 3: Objectives
Identify and describe important entities and relationships to model data
Describe important data models used in Hydrology such as the Observations Data Model (ODM), ArcHydro, and NetCDF

## Slide 4: What is a Data Model?

## Slide 5: What is a Data Model?
Abstract model that documents and organizes data
Explicitly provides the definition of and determines the structure of data
Used as a plan and structure for developing applications that use the data

## Slide 6: Data Models
Define the “entity” types within a domain
Methods (how)
Sites (where)
Values
Data Sources (who)

## Slide 7: Data Models
Define the “attributes” of entities
Entity = Site
Attributes Values
Site Name: Little Bear River near Wellsville
Site Code: USU-LBR-Wellsville
Latitude: 41.643457
Longitude: -111.917649
Elevation: 1365 m
State: Utah
County: Cache
Description: Attached to SR101 bridge.
Site Type: Stream

## Slide 8: Data Models
Define the relationships among entities
Water temperature values in degrees Celsius measured in the Little Bear River at Mendon Road using a Hydrolab MS5 multiparameter sonde by Utah State University
Site
Variable and Method
Source
Values

## Slide 9: Data Models
Define the “business rules” for data
  Observations are recorded at one and only one site
  One or more variables are measured at a site
  A site must have a name
  A variable name must be chosen from a controlled vocabulary

## Slide 10: What are the different types of data models?

## Slide 11: Types of Data Models
Relational data models – e.g., relational databases
1
*
*
1

## Slide 12: Types of Data Models
File based data models
  ESRI File Geodatabase
  NetCDF
Structured file or set of files that store data

## Slide 13: Types of Data Models
Extensible Markup Language (XML) schemas

## Slide 14: Object Model
Class/Object
Properties
Methods
Types of Data Models

## Slide 15: What are some data models commonly used in Hydrology?

## Slide 16: Observations Data Model (ODM)
Soil
moisture
data
Streamflow
Flux tower data
Groundwater
levels
Water Quality
Precipitation
& Climate
A relational database at the single observation level
Metadata for unambiguous interpretation
Traceable heritage from raw measurements to usable information
Promote syntactic and semantic consistency
Cross dimension retrieval and analysis
Horsburgh, J. S., D. G. Tarboton, D. R. Maidment, and I. Zaslavsky (2008), A relational model for environmental and water resources data, Water Resources Research, 44, W05406, doi:10.1029/2007WR006392.

## Slide 17: What are the basic attributes to be associated with each single data value and how can these best be organized?
Space, S
Time, T
Variables, V
s
t
vi
vi (s,t)
“Where”
“What”
“When”
A data value
Variable
Method
Quality Control Level
Sample Medium
Value Type
Data Type
Source/Organization
Units
Accuracy
Censoring
Qualifying comments
Location
Feature of interest
DateTime
Interval (support)

## Slide 18: Data Series – A Time Series of Hydrologic Observations
Space
Variable, Vi
Site, Sj
End Date Time, t2
Begin Date Time, t1
Time
Variables
Count, C
There are C measurements of Variable Vi at Site Sj from time t1 to time t2
Defined by unique combinations of:
Site
Variable
Method
Source
Quality Control Level

## Slide 19
ODM 1.1.1
Sites
(where)
Variables
(what)
Methods
(how)
Sources
(who)
Quality Control Levels
Values +
(when)

## Slide 20: ODM Example: Water Quality from a Profile in a Lake
Notes: Water Chemistry From a Lake Profile
Concepts:
Grouped observations (all observations in one reservoir profile)
Observations made using an offset (observations made at multiple depths below the surface of a reservoir)
Observations made using a specific method (observations made using a particular field instrument)
Relationships:
Relationship between Values table and the Variables table on VariableID
Relationship between Values table and OffestTypes table on OffsetTypeID
Relationship between Values table and Methods table on MethodID
Relationship between Variables table and Units table on UnitID
Relationship between GroupDescriptions table and Groups table on GroupID
Relationship between OffsetTypes table and Units table on UnitID and OffsetUnitID

## Slide 21: Arc Hydro: GIS for Water Resources
Arc Hydro
  An ArcGIS data model for water resources
  Arc Hydro toolset for implementation
  Framework for linking hydrologic simulation models
The Arc Hydro data model and
application tools are in the public
domain
Published in 2002, now in revision for Arc Hydro II
Notes: Notes:
Industrial partners: ESRI, Danish Hydraulic Institute, Camp,Dresser and McKee, Dodson and Associates
Government partners:
Federal: EPA, USGS, Corps of Engineers (Hydrologic Engineering Center)
State: Texas Natural Resource Conservation Commission, Texas Water Development Board
Local: Lower Colorado River Authority, City of Austin, Dept of Watershed Protection
Academic Partners: University of Texas, Brigham Young University, Utah State University

## Slide 22
Streams
Watersheds
Waterbody
Hydro Points
Arc Hydro Framework Input Data
Notes: The Arc Hydro Framework is a simplified version of the full Arc Hydro data model designed for an entry level user who just wants to put together a basic data set for streams, watersheds, waterbodies and hydro points like stream gages and water quality monitoring points

## Slide 23
Arc Hydro Framework
Data Model
Notes: The Arc Hydro framework is built on a Hydro Network made up of HydroEdges (stream lines) and HydroJunctions (points of interest on the lines). The watersheds, waterbodies and hydropoints are connected to the hydronetwork using relationships with the hydro junctions (blue lines in the diagram).

## Slide 24: What Can I do with ArcHydro?
ArcHydro defines flow lines and junctions and encodes flow directions
ArcHydro encodes relationships among watersheds, streams, and junctions
Establishes hydrologic connectivity between polygon catchments (polygons), stream reaches (lines), and junctions (points)

## Slide 25: What Can I Do with ArcHydro?
Network Tracing
Select all streams above a point
Select the downstream path for a point

## Slide 26: Arc Hydro Groundwater
Data model and tools for managing groundwater data in ArcGIS
Notes: Notes:
Industrial partners: ESRI, Danish Hydraulic Institute, Camp,Dresser and McKee, Dodson and Associates
Government partners:
Federal: EPA, USGS, Corps of Engineers (Hydrologic Engineering Center)
State: Texas Natural Resource Conservation Commission, Texas Water Development Board
Local: Lower Colorado River Authority, City of Austin, Dept of Watershed Protection
Academic Partners: University of Texas, Brigham Young University, Utah State University

## Slide 27: Arc Hydro GW Data Model
Notes: This is an overview diagram of the AHGW data model.
You can review the different components, talk about what each component is for:
Framework – includes hydrography, monitoring points, wells, aquifers, tables for managing time series (the framework includes a simplified temporal component). – with the framework you can get started on most water resources projects.
Borehole data – description of vertical information recorded along boreholes (hydrostratigraphy, well construction).
Geology – representation of data from geologic maps.
Hydrostratigraphy – building 2D and 3D hydrogeologic models including surfaces, cross sections, volumes.
Temporal – dealing with time varying data – plots, tracks, animations.
Simulation – integration with groundwater simulation models, especially MODFLOW.

## Slide 28: NetCDF
A platform independent format for representing multi-dimensional, array-orientated scientific data
Continuous space-time data model
  Both time and space are varying
Especially useful for time-varying grids
  Time varying precipitation fields (e.g., radar rainfall data)
Used extensively in the weather and climate domains

## Slide 29: Multidimensional Data
Time = 1
Time = 2
Time = 3
http://www.unidata.ucar.edu

## Slide 30: Multidimensional Data – Space and Time

## Slide 31: Data Modeling
Goal – make sure all data objects required by a database are completely and accurately represented
Data model design – the blueprint for creating a physical implementation of a database

## Slide 32: Data Modeling Terms
Entity – a class of real world objects having common attributes (e.g., sites, variables, methods).
Attribute – A characteristic or property of an entity (site name, latitude, longitude)
Relationship – an association between two or more entities
Cardinality – the number of entities on either end of a relationship (one-to-one, one-to-many, many-to-many, etc.)

## Slide 33: Data Modeling Exercise
Consider:
  What is the “entity”?
  What are the “attributes” of the entity?

## Slide 34: Data Modeling Exercise
What is the entity?
What are the attributes?

## Slide 35: Data Modeling Exercise
What is the entity?
What are the attributes?

## Slide 36: Data Modeling Exercise
What are the relationships?
Apple
Apple Tree
Orchard
Grows On
Grows In

## Slide 37: Data Modeling Exercise
What are the relationships?
Apple
Apple Tree
Orchard
Grows On
Grows In
What about the business rules?

## Slide 38: Assignment 3 Data
Multiple Monitoring Sites
Multiple Sensors at Each Site
1 or More Time Series Per Sensor
3 Different Watersheds

## Slide 39: Assignment 3 Data
Site Information
Variable and Method Information
Source Information
Data Table

## Slide 40: Assignment 3
A group of researchers recently deployed several instruments to continuously monitor streamflow and water quality at multiple monitoring sites in 3 watersheds located in northern Utah. The instruments report measurements in numerous datalogger data files that the researcher must now regularly retrieve, organize, quality-control/quality-check, aggregate, and manipulate before they can perform further analysis.
Design a logical data model to represent the data and its associated metadata
Use MySQL Workbench to create an entity relationship diagram of your data model

## Slide 41: Data Model Design
Our focus – relational data model design
Three stages:
  Conceptual data model
  Logical data model
  Physical data model

## Slide 42: Conceptual Data Model (AKA – The Information Model)
High-level description of the data domain
Does not constrain how that description is mapped to an actual implementation in software
There may be many mappings
  Relational database
  Object model
  XML schema, etc.

## Slide 43: Apple/Tree/Orchard Conceptual Model
Apple
Apple Tree
Orchard
Grows On
Grows In

## Slide 44: Hydrologic Time Series
An organization operates a network of monitoring sites. At each site they collect data for a number of time series, and each time series contains a set of observations

## Slide 45: Conceptual Data Model
Defines scope of the domain
Defines and organizes data requirements
Defines entities and relationships among them
Site
TimeSeries
Observations
1
1
*
*
Entities
Relationships

## Slide 46: Defining Entities and Relationships
Instead of beginning with this:
Sometimes its easier to write statements:
  Many TimeSeries are measured at a Site.
  Each TimeSeries contains one or more Observations.
The nouns become entities and the verbs become relationships.
Site
TimeSeries
Observations
1
1
*
*

## Slide 47: Considerations in Modeling Data
What is the information/data domain that you are modeling?
Is there an existing data model that will work?
What are the 20 queries that you want to do?
  e.g., “Give me simultaneous observations of turbidity and TSS collected during the spring snowmelt period so I can develop a regression in R.”
What software do you want (have) to use?
How do you want to share the data?

## Slide 48: Advantages of Formal Data Models
Provide a high degree of structure to data
Generally implemented in software that has robust querying, manipulation, and visualization capabilities (e.g., RDBMS or GIS)
Facilitate software development
Can help in capturing the semantics of data

## Slide 49: Disadvantages
Can be stiff and difficult to change
Difficult to anticipate needs in the design stages
Can be incompatible across organizations
Can become complex

## Slide 50: Summary (1)
A data model provides a definition of a formal structure for data
There are several flavors of data models, each with different strengths, weaknesses, and appropriate uses
Data models can facilitate software development

## Slide 51: Summary (2)
Common data models used in hydrology
  The CUAHSI Observations Data Model (ODM) provides an organizational structure for hydrologic time series data
  Arc Hydro is a geographic data model for surface hydrologic features
  ArcHydro Groundwater adds subsurface hydrologic features, geology, borehole data, and hydrostratigraphy
  NetCDF combines both geospatial and temporal domains into a continuous space-time data model

## Slide 52: References and Credits
Horsburgh, J.S., D.G. Tarboton (2012). CUAHSI Community Observations Data Model (ODM) Version 1.1.1 Design Specifications, CUAHSI, Washington, D.C, http://www.codeplex.com/Download?ProjectName=HydroServer&DownloadId=349176
Horsburgh, J. S., D. G. Tarboton, D. R. Maidment, and I. Zaslavsky (2008), A relational model for environmental and water resources data, Water Resources Research, 44, W05406, http://dx.doi.org/10.1029/2007WR006392.
Maidment, D.R. (ed.) (2002). Arc Hydro GIS for Water Resources, ESRI Press, Redlands, CA, 203 p.
Strassberg, G., N.L. Jones, D.R. Maidment (2011). Arc Hydro Groundwater GIS for Hydrogeology, ESRI Press, Redlands, CA, 160 p.
Credits:
Arc Hydro slides used with permission from David Maidment, University of Texas at Austin.
ArcHydro Groundwater slides used with permission from Norm Jones, Brigham Young University/Aquaveo.

## Slide 53: Exercise: Conceptual Data Model
Multiple Monitoring Sites
Multiple Sensors at Each Site
1 or More Time Series Per Sensor
3 Different Watersheds