## Slide 1: Infiltration and unsaturated flow
Learning objective
Be able to calculate infiltration, infiltration capacity and runoff rates using the methods described in the Rainfall Runoff workbook chapter 5 and Dingman chapter 6.

## Slide 2: Problem 1 as an example

## Slide 3
Table 1. Clapp and Hornberger (1978) parameters for equation (27) based on analysis of 1845 soils. Values in parentheses are standard deviations |  |  |  | 
Soil Texture | Porosity | Ks (cm/hr) | psi_ae (cm) | b
Sand | 0.395 (0.056) | 63.36 | 12.1 (14.3) | 4.05 (1.78)
Loamy sand | 0.410 (0.068) | 56.16 | 9 (12.4) | 4.38 (1.47)
Sandy loam | 0.435 (0.086) | 12.49 | 21.8(31.0) | 4.9 (1.75)
Silt loam | 0.485 (0.059) | 2.59 | 78.6 (51.2) | 5.3 (1.96)
Loam | 0.451 (0.078) | 2.50 | 47.8 (51.2) | 5.39 (1.87)
Sandy clay loam | 0.420 (0.059) | 2.27 | 29.9 (37.8) | 7.12 (2.43)
Silty clay loam | 0.477 (0.057) | 0.612 | 35.6 (37.8) | 7.75 (2.77)
Clay loam | 0.476 (0.053) | 0.882 | 63 (51.0) | 8.52 (3.44)
Sandy clay | 0.426 (0.057) | 0.781 | 15.3 (17.3) | 10.4 (1.64)
Silty clay | 0.492 (0.064) | 0.371 | 49 (62.01) | 10.4 (4.45)
Clay | 0.482 (0.050) | 0.461 | 40.5 (39.7) | 11.4 (3.7)

## Slide 4: The class of problem we need to solve
Consider a soil of given type (e.g. silty clay loam) and given an input rainfall hyetograph, calculate the infiltration and the runoff.
Rainfall rate 2 cm/hr, for 3 hours
Initial soil moisture content 0.3

## Slide 5
Surface Runoff occurs when surface water input exceeds infiltration capacity. (a) Infiltration rate = rainfall rate which is less than infiltration capacity. (b) Runoff rate = Rainfall intensity – Infiltration capacity. (from Dunne and Leopold, 1978)

## Slide 6
Saturation excess runoff generation mechanism
Water table near surface
Finite volume of water can infiltrate before soil completely saturated
No further infiltration
All further precipitation is runoff
Occurs in lowlands, zones of convergent topography
Partial contributing area concept
Dunne Mechanism
Saturation from Below
Notes: Figure 38. Saturation excess runoff generation mechanism. (a) Moisture content versus depth profiles, and (b) Runoff generation time series. (from Bras, 1990)

## Slide 7
(a)
(b)
Infiltration excess runoff generation mechanism
Initially dry soil
Suction large at surface
Total head gradient large
Large infiltration capacity
Penetration of moisture from rainfall
Suction reduces
Infiltration capacity reduces
Excess precipitation becomes runoff
Saturation from Above
Horton Mechanism
Notes: Figure 37. Infiltration excess runoff generation mechanism. (a) Moisture content versus depth profiles and (b) Runoff generation time series. (from Bras, 1990)

## Slide 8
Wetting front in a sandy soil exposed after intense rain (from Dingman, 1994).
Preferential pathway infiltration (Markus Weiler, ETH Zurich)
Need Equations to describe reduction in infiltration capacity as depth of water that has infiltrated increases (wetting front propagates downwards), recognizing that this may be a simplification

## Slide 9
Continuity equation in an unsaturated porous medium.
 x y z =
(q x y – (q+q) x y) t

## Slide 10
qy
qy+qy
qx+qx
z z
z
qx
3 dimensional continuity equation.

## Slide 11: Richard's Equation
h = +z
Continuity
Darcy
Pressure and elevation head
Soil moisture characteristic
Specific moisture capacity
Pressure head as independent variable

## Slide 12: Diffusion form of Richard's Equation
Soil water Diffusivity

## Slide 13
Moisture content, 
0.5
0.4
0.3
0.2
0.1
Depth, z, (cm)
10
20
30
40
t1
t2
t3
t4
L

Initial moisture content o
Saturation moisture content s equivalent to porosity, n
Green-Ampt model idealization of wetting front penetration into a soil profile
Notes: Figure 37. Green-Ampt model idealization of wetting front penetration into a soil profile.

## Slide 14
Infiltration example problem
Consider a soil of given type (e.g. silty clay loam) and given an input rainfall hyetograph, calculate the infiltration and the runoff. Initial soil moisture content 0.3. Rainfall rate 2 cm/hr, for 3 hours.

## Slide 15: Infiltrability – Depth Function

## Slide 16: Key Ideas
Richard’s equation governs the movement of water in the unsaturated zone
The Green Ampt Model assumes a sharp wetting front and leads to the Infiltrability-Depth approximation
The state of the system in calculating infiltration is described by the depth of water that has infiltrated. This is the basis for the methods that follow.

## Slide 17
Cumulative infiltration at ponding
Time to ponding
Infiltration under ponded conditions

## Slide 18
Soil Texture | Porosity n | Effective porosity e | Wetting front soil suction head ¦f¦ (cm) | Hydraulic conductivity Ksat (cm/hr)
Sand | 0.437 (0.374-0.500) | 0.417 (0.354-0.480) | 4.95 (0.97-25.36) | 11.78
Loamy sand | 0.437 (0.363-0.506) | 0.401 (0.329-0.473) | 6.13 (1.35-27.94) | 2.99
Sandy loam | 0.453 (0.351-0.555) | 0.412 (0.283-0.541) | 11.01 (2.67-45.47) | 1.09
Loam | 0.463 (0.375-0.551) | 0.434 (0.334-0.534) | 8.89 (1.33-59.38) | 0.34
Silt loam | 0.501 (0.420-0.582) | 0.486 (0.394-0.578) | 16.68 (2.92-95.39) | 0.65
Sandy clay loam | 0.398 (0.332-0.464) | 0.330 (0.235-0.425) | 21.85 (4.42-108.0) | 0.15
Clay loam | 0.464 (0.409-0.519) | 0.309 (0.279-0.501) | 20.88 (4.79-91.10) | 0.1
Silty clay loam | 0.471 (0.418-0.524) | 0.432 (0.347-0.517) | 27.30 (5.67-131.50) | 0.1
Sandy clay | 0.430 (0.370-0.490) | 0.321 (0.207-0.435) | 23.90 (4.08-140.2) | 0.06
Silty clay | 0.479 (0.425-0.533) | 0.423 (0.334-0.512) | 29.22 (6.13-139.4) | 0.05
Clay | 0.475 (0.427-0.523) | 0.385 (0.269-0.501) | 31.63 (6.39-156.5) | 0.03
Green – Ampt infiltration parameters for various soil classes (Rawls et al., 1983). The numbers in parentheses are one standard deviation around the parameter value given.

## Slide 19: Philip Model

## Slide 20
Cumulative infiltration at ponding
Time to ponding
Infiltration under ponded conditions

## Slide 21
t1
to
t0
Time Compression Approximation
Notes: Figure 40. Partition of surface water input into infiltration and runoff using the Horton infiltration equation. Ponding starts at t1. The cumulative depth of water that has infiltrated up to this time is the area F1 (shaded gray). This is less than the maximum possible infiltration up to t1 under the fc(t) curve. To accommodate this the fc(t) curve is shifted in time by an amount to so that the cumulative infiltration from to to t1 (hatched area) equals F1. Runoff is precipitation in excess of fc(t-to) (blue area).

## Slide 22: Horton Infiltration Model

## Slide 23
Cumulative infiltration at ponding
Time to ponding
Infiltration under ponded conditions
Given Fs, ts solve for to implicitly then use 2nd equation

## Slide 24
f0
f1
t1
to
F1
t0
Notes: Figure 40. Partition of surface water input into infiltration and runoff using the Horton infiltration equation. Ponding starts at t1. The cumulative depth of water that has infiltrated up to this time is the area F1 (shaded gray). This is less than the maximum possible infiltration up to t1 under the fc(t) curve. To accommodate this the fc(t) curve is shifted in time by an amount to so that the cumulative infiltration from to to t1 (hatched area) equals F1. Runoff is precipitation in excess of fc(t-to) (blue area).

## Slide 25
Time
Surface Water Input
Infiltration Capacity
Runoff
Runoff
Notes: Figure 41. Pulse runoff hyetograph obtained from surface water input hyetograph and variable infiltration capacity.

## Slide 26
Initialize: at t = 0, Ft = 0
Is fc £ wt
fc> wt
fc £ wt
No ponding at the beginning of the interval. Calculate tentative values
and column 1.
Ponding occurs throughout interval: Ft+Dt calculated using infiltration under ponded conditions equations with ts=t and Fs= Ft.
Column 3.
Ponding starts during the interval. Solve for Fp from wt, column 2.
Dt' = (Fp-Ft)/wt
Ft+Dt calculated using infiltration under ponded conditions equations with ts=t+Dt' and Fs= Fp. Column 3.
No ponding throughout interval
Increment time t=t+Dt
Calculate infiltration capacity fc from Ft, column 1 of table.
A
C
B
D
E
Infiltration is ft = Ft+Dt-Ft
Runoff generated is rt= wtDt - ft
F
G
Notes: Figure 42. Flow chart for determining infiltration and runoff generated under variable surface water input intensity.

## Slide 27
Equations for variable surface water input intensity infiltration calculation.

## Slide 28
0.00005
0.146
0.303
0.159
0.178
Notes: Figure 43. Rainfall Hyetograph, Infiltration Capacity and Runoff Generated in Example 1. Numbers are infiltration in cm in each interval.

## Slide 29
0.032
0.282
0.249
0.289
0.004
Notes: Figure 44. Rainfall Hyetograph, Infiltration Capacity and Runoff Generated in Example 2. Numbers are infiltration in cm in each interval.

## Slide 30
0.0003
0.165
0.080
0.119
Notes: Figure 45. Rainfall Hyetograph, Infiltration Capacity and Runoff Generated in Example 3. Numbers are infiltration in cm in each interval.

## Slide 31
Baseflow Separation Techniques
From Chow, V. T., D. R. Maidment and L. W. Mays, (1988), Applied Hydrology, McGraw Hill, 572 p.

## Slide 32
Phi () - index

## Slide 33: Determining the  index and Excess Rainfall Hyetograph

## Slide 34: Direct Runoff from the SCS Curve Number Equation